## Slide 2
NALMCO 2024 LEARNING LAB
LIGHTING CONTROLS BEYONG BASIC ENERGY SAVINGS
Doug White Eric Fournier

## Slide 3: Agenda
BASIC Energy Saving Control Strategies
ADVANCED Energy Saving Control Strategies
NON-ENERGY Benefits (NEBs) Control Strategies
Case Studies

## Slide 4: BASIC ENERGY SAVINGS CONTROL STRATEGIES

## Slide 5: CONTROLS PROVIDE THE FOLLOWING FIVE BASIC FUNCTIONS
Manual Controls give occupants the ability to manually turn lights On/Off/Dim or Recall Scenes
Occupancy Sensors turn lights on/off automatically when occupants enter and leave a space
High-End Trim sets an artificial maximum light level below 100%
Typ. Energy Savings
10-20%
PRODUCE THE RIGHT AMOUNT OF LIGHT
BY CONTROLLING LIGHT OUTPUT INTENSITY
WHERE THE LIGHT IS NEEDED
BY DECIDING ZONE vs. LUMINAIRE CONTROLS
Typ. Energy Savings
10-30%
WHEN THE LIGHT IS NEEDED
AUTOMATICALLY REDUCING ELECTRIC LIGHTS WHEN SPACE IS UNOCCUPIED OR WELL LIT
Typ. Energy Savings
20-60%
Daylight Harvesting dims electric lights when daylight is available to light the space
Scheduling/Timeclock provides changed in light levels based on time of the day/night
Typ. Energy Savings
25-60%
Typ. Energy Savings
10-20%
Know the Difference…
In Occupancy mode, fixtures automatically turn lights on and off as occupancy is detected
In Vacancy Mode, the user must physically turn the lights on using Manual Controls
Notes: The WHAT vs. the HOW…

## Slide 6: ADVANCED ENERGY SAVINGS CONTROL STRATEGIES

## Slide 7: LIGHTING CONTROLS ARE EVOLVING TO PROVIDE ADVANCED FUNCTIONS
TELL YOU HOW YOUR LIGHTS ARE PERFORMING
INTELLIGENT CONTROL SYSTEMS WITH MEASURING AND MONITORING
Energy Monitoring provide real time energy data for each fixture or an entire circuit
Fun Facts…
Some Utility companies like Consumer Energy in MI offer higher rebates upon providing before/after energy data reports
SIMPLIFY & REDUCE EMERGENCY LIGHTING COST
FOLLOWING NEW UL 924-2022 CODE
Emergency Lighting Controls offer continuous detection of normal power and trigger Emergency mode upon power loss
Notes: Lighting controls are evolving to provide advanced functions, which vary in availability depending on system type and application need
With the release of the May 2022 update to UL 924, UL has changed how emergency lighting works in significant ways. In the past, a circuit level device would detect turn-on of emergency power and trigger the lights to stay on at full for 90 minutes, non by-passable.
Now, UL 924 requires active and continuous detection of normal power. Emergency mode is now triggered by the loss of normal power, just for the duration of that loss, vs a specified time frame. Devices that passively detect either the presence of emergency power, or the interruption of normal power to trigger emergency mode are no longer allowed.

## Slide 8: LIGHTING CONTROLS ARE EVOLVING TO PROVIDE ADVANCED FUNCTIONS
BMS/HVAC integration
Load Shedding
REDUCE PLUG LOADS & HVAC CONSUMPTION
LEVERAGING CONTROLS & SENSORS
Plug Load Controls automatically turn off controlled receptacles once occupants leave a space
COMMUNICATE WITH UTILITY SERVERS
TO MINIMIZE PRESSURE ON THE GRID
HVAC/BMS Integration controls heating, ventilation, and air conditioning systems through contact closure, BACnet protocol or API integration
Load Shedding/Demand Response automatically and temporarily reduces lighting loads during peak electricity usage times

## Slide 9: WHY INTEGRATING SYSTEMS
BMS/HVAC integration
Load Shedding
Lighting and HVAC consume more than half of building energy use
The meter is on the building – not on each system, so why are these systems designed and controlled in silos?
Control both HVAC and lighting systems using one platform – more functionality with smoother ease of operations
Integrating systems brings the most value and the deepest energy savings

## Slide 10: LIGHTING & HVAC INTEGRATION
BMS/HVAC integration
Load Shedding
Controllable lighting offers increased energy savings, comfort and flexibility
Use BAS to control HVAC and lights with shared schedules
Use occupancy data to control the lighting and HVAC system through the BAS for additional savings
Aggregate HVAC and lighting energy reporting through BAS for one energy dashboard
Deploy demand response signals to both HVAC and lighting systems during an event

## Slide 11: THEY ALLOW FOR REMOTE PROGRAMMING AND REMOTE ACCESS
Eliminate end-user disruption during programming
Increase flexibility for when to perform lighting and control upgrades
Reduce overall programming cost
Offer Faster response time
Deliver more effective diagnose & repair methods

## Slide 12: NON-ENERGY BENEFTIS (NEBs) CONTROL STRATEGIES

## Slide 13: FOCUS ON THE BIG IMPACT and APPLY THE 3-30-300 RULE
$3…Utility
$30…Rent
$300… Employee Costs (Salary, Benefits, etc.)
Facility Mgr’ often focus on the 3 and 30 sections, while C-suites also value the importance of the 300
  Happiness
  Productivity
  Wellness
  Well lit space, ample daylight, etc.
Notes: Study conducted by JLL
This rule provides a breakdown of what an organization pays per square foot in terms of total occupancy cost.

## Slide 14: SMARTER BUILDINGS LEVERAGE DATA & FOCUS ON CUSTOMER EXPERIENCE
Understand how people use spaces to build better collaborative spaces
Right-size commercial buildings
Analyze occupant interaction with their smart lighting system and personal preferences

## Slide 15: NON-ENERGY BENEFITS (NEB) CONTROL STRATEGIES
Know the Difference…
In Color Tuning, color temperature (CCT) is automatically programmed to change throughout day/night or is adjusted at any time using wall stations
In Color Selectable, the user must physically select the CCT directly on the fixture (usually via dip switch). Set & Forget operation
PRODUCE THE RIGHT COLOR OR SHADE OF LIGHT
BY SEPARATING LIGHT INTENSITY FROM COLOR TEMPERATURE (CCT)
Color Tuning/Tunable White manually or automatically adjust the color temperature based on space occupancy and/or time of the day

## Slide 16: INCREASE IN SAFETY MEASURES
EMERGENCY LOCK DOWN MODE

## Slide 17
STATE FARM BUILDINGS - TEMPE, AZ
~ 6,200 fixtures controlled individually
23 floors, all common areas, private offices, conf. rooms and open offices
High End trim, occupancy sensors and manual controls
BACnet integration
CASE STUDY #1… BMS INTEGRATION

## Slide 18: DOE ILC 2023 Award Winning Project
ORTEGA MIDDLE SCHOOL - ALAMOSA, CO
Largest school district in San Luis Valley ASD
Student achievement data fell into turnaround status for OMS
School had 2 classrooms with color tuning in special needs; they liked it and expanded it a year later to the entire school
When it came time to abate asbestos and a new ceiling grid would be installed, the project was designed around color tuning to provide opportunities for every student
CASE STUDY #2…
TUNABLE WHITE

## Slide 19
WSSB – WASHINGTON STATE SCHOOL FOR THE BLIND, WA
All classrooms
Fully automated CCT changing throughout the day with manual override capabilities impact kids’ ability to learn
CASE STUDY #3…
AUTOMATED CIRCADIAN LIGHTING

## Slide 20
RUSH UNIVERSITY MEDICAL CENTER - CHICAGO, IL
10 floors, 8 fully controlled, ~ 2,000 fixtures retrofitted
Lights were too bright in classrooms and offices
Lighting Controls added to multiple lighting fixture brands
Controls needed to be “fixture agnostic” and non-proprietary to specific lighting brands
Cost effective, flexible, robust and future proof for Demand Response
CASE STUDY #4… DIMMING, FLEXIBILITY AND DEMAND REPONSE

## Slide 21: DOE ILC 2022 Award Winning Project
Project Location: Lansing, MI
K-12 Holt School District; 9 schools
340,000sqft High School only
10,000+ fixtures; ~8,000 Bluetooth Lighting Controls
School now considering smart door locks and wanting integration with Network Lighting Control system
CASE STUDY #5…
SAFETY MEASURES

## Slide 22: QUESTIONS?
THANK YOU!
Doug White
Energy Services Product Manager, Lighting Commercial HVAC Americas
Doug.White@tranetechnologies.com
303.253.0496
Eric Fournier
VP Business Development
Eric.Fournier@avi-on.com
760.889.8151